## Slide 1: Doppler Techniques
Nico Sneeuw
Mohammad Tourian
Institute of Geodesy
University of Stuttgart
Satellite Geodesy Observation Techniques, MSc G&G
WS2019/2020, Stuttgart
Notes: TBD: Folie mit „Schwebung“:
Grafik mit Superposition zweier Sinuswellen
Formel sin(f_1*t) + sin(f_2*t) =…

## Slide 2: table of content
Doppler principle
observation equation
DORIS implementation
  ground segment
  space segment
products / applications

## Slide 3: principle

## Slide 4: Christian Doppler (18031853)
Austrian mathematician / physicist
physically unfit to take over family business (stonemason)
1841: professor of physics and mathematics at Charles University, Prague
1842: Über das farbige Licht der Doppelsterne und einiger anderer Gestirne des Himmels
1850: Direktor, Institute of Physics at University Vienna (1st professor of experimental physics)
Wikipedia

## Slide 5: Doppler effect
source infinitely far away
source far away
observer near source
source “through” observer
Seeber, Satellite Geodesy
time of closest approach
(TCA)

## Slide 6: Doppler effect under arbitrary angle
received frequency (variable)
sender frequency (stable)
angle between velocity vector and line source-receiver

## Slide 7: Doppler effect under arbitrary angle
received frequency (variable)
sender frequency (stable)
radial velocity
under :
A. Kleusberg (1984)
Diagnose und Therapie von geodätischen Satellitennetzen vom Typ Doppler
DGK C293

## Slide 8: observation equation

## Slide 9: observation equation (1/4)
Doppler frequency shift
Numerical example, e.g. @

## Slide 10: observation equation (2/4)
Subtract Doppler-shifted frequency from stable frequency , generated in receiver. Choose such that
beat frequency is always positive.
Frequencies are hard to observe. Phase observations (zero-crossings or fringes) are easier

## Slide 11: observation equation (3/4)
Integrated Doppler count
With , etc.
generated in receiver
beat frequency
emitted time marks
= emitted time mark, when emitted by sender
= emitted time mark, when it reaches the receiver

## Slide 12: integrated Doppler count visualized
Seeber, Satellite Geodesy

## Slide 13: observation equation (4/4)
#cycles transmitted between and equals #cycles received between time marks and .
observation equation
1 observation, 4 unknowns, orbit considered known
atmospheric and relativistic terms ignored here

## Slide 14: Error Budget and Corrections
Orbit errors: predicted ephemerides differ from true satellite positions
Atmospheric refraction: the signla propagation is not in vacuum
Signal processing in the reciever
  Ionospheric refraction
  Tropospheric correction: wet, dry
Aberration: Earth rotation while the signal propagation
Relativistic effects

## Slide 15: Atmospheric refraction
Ionospheric refraction
  Single frequency
  Double frequency
+ +
First-order
contribution
Observed Doppler count
True Doppler count
/

## Slide 16: Transit implementation
see Seeber, Section 6.2

## Slide 17: DORIS implementation

## Slide 18: DORIS
Doppler principle upside-down, i.e.
  stable frequency at ground stations (beacons)
  receiver (Doppler count measurement) at satellite
developed by the French space agency CNES (Centre National d’Études Spatiales) in cooperation with IGN and GRGS
1990 first realization of the system onboard the remote sensing satellite mission SPOT-2
original purpose: precise orbit determination
The average precision of the range rate observations is about 0.30.5 mm/s
positioning not instantaneous (post-processing required)

## Slide 19: DORIS system overview

## Slide 20: ground segment

## Slide 21
as on May 2012

## Slide 22: global DORIS network
about 60 sites

## Slide 23: visibility

## Slide 24: ground beacons
Mount Stromlo - Australia
Toulouse - France
Syowa - Antarctica (Japan)
Yellowknife - Canada

## Slide 25: ground segment
main signal frequency 2036.25 MHz
secondary frequency 401.25 MHz (used for ionospheric correction)
continuous and omnidirectional signals
Receiver onboard the satellite receives signal and measures Doppler shift over a short count interval, e.g. 10 seconds
Data are time tagged with respect to an ultra-stable onboard crystal oscillator
control segment: master beacon and control center in Toulouse, France

## Slide 26: space segment

## Slide 27: DORIS-equipped satellites
COSPAR # | Satellite name | Launch date | Perigee (km) | Apogee (km) | T (min) | I (deg) | e | DORIS receiver generation | Other tracking system | DORIS instrument end | Mission End
9000501 | SPOT-2 | 22-Jan-1990 | 802 | 831 | 100.9 | 98.7 | .002014 | 1G | - | 29-Jul-2009 | 29-Jul-2009
9205201 | TOPEX/ POSEIDON | 10-Aug-1992 | 1322 | 1341 | 112.0 | 66.5 | .000095 | 1G | SLR+GPS | 1-Nov-2004 | 9-Oct-2005
9306101 | SPOT-3 | 26-Sep-1993 | 819 | 846 | 101.2 | 98.6 | .001872 | 1G | - | 9-Nov-1996 | 14-Nov-1996
9801701 | SPOT-4 | 24-Mar-1998 | 791 | 811 | 100.9 | 98.8 | .001392 | 1G | - |  | 24-Jun-2013
0105501 | JASON-1 | 7-Dec-2001 | 1328 | 1340 | 112.0 | 66.0 | .000778 | 2GM | SLR+GPS |  | 21-Jun-2013
0200901 | ENVISAT | 1-Apr-2002 | 785 | 791 | 100.6 | 98.6 | .000419 | 2G | SLR | 8-Apr-2012 | 9-May-2012
0202101 | SPOT-5 | 4-May-2002 | 825 | 826 | 101.4 | 98.8 | .000069 | 2GM | - |  | 
0700604 | STPSat-1 | 9-Mar-2007 | 558 | 561 | 95.8 | 35.4 |  | CITRIS | GPS |  | 7-Oct-2009
0803201 | JASON-2 | 20-Jun-2008 | 1328 | 1340 | 112.0 | 66.0 | .000702 | DGXX | SLR+GPS |  | 
1001301 | CRYOSAT-2 | 8-Apr-2010 | 707 | 727 | 99.4 | 92.0 | .001407 | DGXX | SLR |  | 
1104301 | HY-2A (Haiyang 2A) | 15-Aug-2011 | 963 | 963 | 104.4 | 99.4 | .00117 | DGXX | SLR+GPS |  | 
1300901 | SARAL | 25-Feb-2013 | 706 | 772 | 99.59 | 98.65 | .001165 | DGXX | SLR |  | 

## Slide 29: products / applications

## Slide 30: products / applications
precise orbit determination (orbitography)
  real-time accuracy ~ 1 m
  with 48 h latency: sub-meter accuracy
  post-processing: sub-dm accuracy; ~ 1 cm for radial direction
positioning of DORIS beacons
  permanent network accuracy ~ 1 cm and 1 mm/year
  contribution to ITRFxx
  dedicated beacons (users) ~ 12 dm
geodesy/geodynamics
  plate tectonics
  Earth rotation parameters
  geocenter motion
  ionosphere
time transfer

## Slide 31: further reading
Seeber (2003), Satellite Geodesy
  Doppler in general: chapter 6
  DORIS: section 6.7
A. Kleusberg (1984) Diagnose und Therapie von geodätischen Satellitennetzen vom Typ Doppler, Deutsche Geodätische Kommission, C293
International DORIS Service http://ids-doris.org/
http://www.aviso.oceanobs.com/en/doris.html